Netting
(LittleLab)

Version 1.1
December 2012

Proprietary and confidential
# Introduction
The praxis illustrates some of the networking capabilities of our nodes and the communication aspects of applications built with them. Note that it doesn't demonstrate everything, like, for example, all the low-level RF communication options (some of which may prove advantageous in specific situations), or even all the higher-level features that our “production” praxes can routinely rely on, e.g., remote node configurations. We have trimmed down the functionality to make things simple and relatively obvious, especially for a novice user.
Every node of the set can (but doesn't have to) be connected (via a USB dongle) to a (virtual) COM port of a PC. On a UNIX (Linux) system, that will be a device named /dev/ttyUSBx. By running any (reasonably flexible) terminal emulator on that port/device you can issue simple commands to the node and receive feedback. The serial parameters of the interface are 9600 bps, 8 bits, no parity, and 1 stop bit, with CR/LF for line termination. Our piter utility[1] is a convenient and flexible terminal emulator, many other emulators can be freely downloaded from the network.
[1] The emulator can be downloaded from http://www.olsonet.com/REPO/piter.zip .
Netting's mode of operation is “set & go”. By this we mean that you first describe the parameters of a message that you may want to transmit (i.e., preset the message), and then use a separate (and trivially simple) command to send that message out as many times as you please. This way, we minimize the number of keystrokes needed to quickly run many potentially interesting test cases. There exist three message types which can be defined and referenced independently. Only one message of a given type can be defined at any given time, but up to three messages (of different types) can coexist. The message types are:
display	A simple message whose role is to be sent to a specific destination (including all destinations, i.e., broadcast, as a special case) and display there a string of characters carried as its payload. The way the message is delivered is up to the network. The multi-hop delivery mechanism is based on our patented TARP scheme.
odr	A message that is supposed to travel a specific path prescribed by the operator (as in Operator Directed Routing). Note that normally our applications do not use this form of communication; it has been implemented for illustration, comparisons, and various networking experiments and demonstrations.
trace	A message to be delivered via TARP, whose actual route is to be tracked and reported. The report is typically produced at the source (based on information carried in a reply message sent by the destination), but there is an option to display the report at the destination.

Any message, regardless of its type, can be turned into a beacon, i.e., be automatically sent at prescribed intervals a specified number of times.
The examples discussed below are based on a model of the LittleLab network expressed in VUEE (our powerful emulator of complete PicOS praxes). It was more convenient for us to generate those examples that way while verifying the network's behaviour in a comfortable virtual setting. We assumed some specific illustrative network configuration providing a handy background for our explanations.
You may rest assured that the examples discussed in the next section do apply to your (real) network. Even though VUEE tests are authoritative, we have verified the network operation with the real nodes as well. Of course, the numerical and quantitative details (the paths taken by packets, the RSS indications, and so on) will depend on the specifics of your node distribution and on the RF propagation conditions in the area.
The model provides built-in terminal emulators of sorts for talking to the virtual UARTs of node models. We call them UART windows. In your case, you will connect to the real nodes via real UART (COM) ports (using the USB-TTL RS232 FTDI cable). The UART windows will be replaced by the windows of your favourite terminal emulator. See Quick Start below.

# Experiments with the VUEE model
The network model used for our experiments is described by the rec10.xml data set and consists of 10 nodes deployed along the perimeter of a 300 x 200 m rectangle, like this:

Note that the model is not some simplistic fake. The application code executed by the virtual nodes is exactly the same as that loaded into the real nodes (at the source code level). You see exactly the same commands and the same kind of responses as you would (will) see in the real network. The virtual wireless channel exhibits qualitatively the same properties as any real RF propagation environment (packets are transmitted and received in finite time depending on their length and transmission rate, the propagation time between a pair of nodes is finite and depends on their distance, the bit error rate is a function of background noise and interference, and so on). Needless to say, your actual (real) wireless channel may exhibit quantitatively different properties, depending on your actual (physical) distribution of nodes, the obstacles, local sources of interference, etc. This may affect the quantitative statistics of packet delivery, but the essence of the system behaviour will remain the same.
Do not execute the actions described in the remainder of this section. Well, you don't have the model, so you cannot execute them anyway. We retain the imperative tone of the section solely as a convenient introduction to the examples.
Execute pip and open the netting project. For that, click File → Open Project in pip's menu, then double click on the netting directory, and press the OK button. Next click Build → VUEE in the menu and wait until the compiler is done. Finally click Execute → Run VUEE to run the model.
The ROAMER window that will pop up after a short while shows a network consisting of 10 nodes numbered from 1 to 10 (as shown in the above figure). Right click on node 5 and select UART (ascii) from the menu. That will bring in a terminal emulator communicating with the UART of node 5. The window will show you the initial sequence of lines produced by the node after reset. That sequence succinctly and schematically lists all the OSS commands recognized by the node, together with their parameters.
Note that you can change the network's geometry (the distribution of nodes) by simply dragging the nodes with the mouse (moving them on the virtual deployment plane). We recommend that you postpone this exercise until later, because moving a node too far from its neighbours may render it unreachable, which in turn may be confusing when trying to follow the examples described below. The initial distribution of nodes tries to make the hops rather clearly pronounced, in the sense that two neighbouring (adjacent) nodes should be able to communicate with each other more or less comfortably, while direct communication between non-adjacent pairs is less likely (albeit not impossible).
Issue a simple command to node 5. In the entry area of its UART window (at the bottom of the window) type h and hit the Enter key. Whenever you issue that command, the node will show you the menu displayed after startup (or reset/reboot). You will see the same menu when you actually reset the node (e.g., with the q command), but then the node will start from scratch having forgotten what it was doing before you hit it.
Try s to see the node status. In response, you will get a line similar to this one:
5 at 34: M 0 at 0 mem 4292.4052.256 bat 2600 trans 0
which says that you are at node number 5 which has been running for 34 seconds (since last power up or reset). The node knows of no master node (this is the M 0 part—more about it later). The amount of free RAM currently available to the node is 4292 words (translating into twice as many bytes) with the minimum that was ever noticed by the node equal to 4052 words. The third number in that sequence (256) shows the minimum number of stack locations (words) noted so far.[2] The three numbers are indications of the node's health when it comes to memory requirements.[3] The second last number (2600) tells the battery status (it is the output of a voltage sensor). The battery should be replaced when the value drops to around 2200. The last number is the binary transient flag, driving display of ODR messages on intermediate nodes.
[2] This value is only meaningfully reported by a real node. For a VUEE model, it is always 256.
[3] Our operating system run by the nodes (PicOS) relies on dynamic memory allocation, e.g., for buffering packets.
## Display messages
We shall start by sending a simple message from node 5 to node 4. For that, we have to define the message first. It will be a simple message of type display (see above). Enter this command in the UART window of node 5:
sd 88 4 0 hello_node_four
The command (set display) presets a message of type display, or should we say the message of type display, because there can only be at most one message of that type preset at any given time. The arguments are, in this order:
- Some number to be sent inside the message (which you can view as a numerical identifier); the size of that number is 4 bytes (large enough to encode millisecond timestamps, for example).
- The destination node ID; in our case it is 4.
- A binary flag (0 or 1) telling whether we want to receive in return an acknowledgement from the recipient. In our case it is 0 meaning “no acknowledgement”.
- A piece of text to be sent in the message along with the numerical identifier. This text cannot contain a space (or rather a space terminates it in the same way as the end of line) and must be shorter than 40 characters.
Whenever you issue sd without arguments, you will see the currently preset display message. For example, following the above definition, an argument-less sd will bring you this:
Disp #88 to 4 ack 0 len 15 <hello_node_four>
It makes sense to open a UART window for node 4 to witness the act of reception. So right click on node 4 in the ROAMER window and (as you did for node 5) select UART (ascii) from the menu. Then, in the UART window for node 5, enter this command:
xd
whose effect is to dispatch from node 5 an instance of the currently defined display message. If everything works fine, you will see a line of text in the UART window of node 4 looking close to this one:
1903: disp #88 fr 5.1 ack 0 15<hello_node_four>
The line says that the node has received a display message with numerical identifier 88 from node 5. The message has travelled a single hop (the 1 following the dot), it doesn't ask to be acknowledged, and it carries the 15-character string “hello_node_four”.
The first number (1903) provide the time stamp of the reception - the recipient's time in seconds counted from the moment of its power up or reset.
To see more hops, send a message to node 2. This time we shall ask for an acknowledgement. Open a UART window at node 2 (to see the reception) and enter these commands at node 5:
sd 89 2 1 a_three_hop_message
xd
You may see at node 2 something like this:
2533: disp #89 fr 5.3 ack 1 19<a_three_hop_message>
and, a short while later:
2533: disp #89 fr 2.3 ack 0 19<a_three_hop_message>
at node 5, which is the echo of the original message (produced by the recipient) arriving back at the sender as an acknowledgement.
Of course, barring a very unlikely coincidence, the time stamps will be different in your case. Note that the coincidence of the time stamps at the sender and the receiver (in the above illustration) should be viewed as irrelevant: it comes as an artifact of the synchronized start up of the model (and all its nodes) at precisely the same time. To make things more realistic, you may reset one of the nodes, say node 2 with the q command and try again.
Generally, you should realize that your results (especially those from multi-hopping experiments) may not be identical to ours, even with a correction for the obvious differences in time stamps. A few paragraphs ago, we said “you may see” rather than “you will see”, because we couldn't be absolutely sure what you would actually see. This is because you are running a reasonably close model of a real network in which individual packets can quite legitimately and stochastically get lost. Even more, the global state of TARP (the multi-hopping scheme) is a complicated and distributed object derived from miscellaneous parameters of past transactions in the network as they have been perceived by the nodes. In some cases, TARP may forward a packet via what seems to be a suboptimal route, and do it differently the next time around, for the very same source-destination pair. Again, this is perfectly normal. Every exploration of a “substandard” path teaches the network something. In fact, this apparent “unpredictability” of TARP is what makes our scheme superior to the traditional point-to-point routing protocols.
The destination of a display message can be zero which means that the message should be broadcast to all nodes in the network.[4] For example, try this from node 5:
[4] Zero can never be a legitimate node ID in our network.
sd 101 0 0 a_broadcast_message
xd
You should see the message reported at all (or almost all—see the note above) nodes. When you ask for acknowledgements (the third argument equal 1), you will receive at node 5 echoes of your message sent back by all the nodes that have received it. Again, as the kind of broadcast service used in this illustration is far from reliable, you should not be surprised by incomplete coverage.
## Beacons
A message (of any type) can be turned into a beacon, which is another way to say that you can send it automatically a certain number of times at certain regular intervals. First, let us define a display message at node 5:
sd 12 10 0 beacon_message
The message is addressed to node 10, i.e., across the full diameter of our network. To turn it into a beacon, enter this (at node 5):
sb d 4 1000
The command defines the beacon to consist of the currently defined display message (the d argument) which will be sent 1000 times at 4-second intervals. Note that this only defines the beacon. To actually start sending it, you have to execute:
ba
which stands for beacon activate. Open a UART window at node 10 to see the messages arrive at their destination. You will see that the number of hops travelled by the beacon varies slightly on different occasions. The beacon can be stopped (before its count runs down) with this command:
bd
which stands for beacon deactivate.
In practical cases involving beacons, the beacons are usually broadcast. Their periodic transmissions compensate for the poor reliability of any single case of a broadcast delivery. For illustration do this (still at node 5):
sd 127 0 0 beacon_for_all
ba
Now you will see the beacon received by (mostly) all nodes.
Note that you do not have to redefine the beacon (the previous setting still holds), only change the display message that the beacon has been mapped to. However, you cannot modify the beacon message while the beacon is active. If you try it, you will get:
Locked
in response, and the command will be ignored.
You can try all the different combinations, e.g., an acknowledged broadcast beacon:
bd
sd 126 0 1 acked_beacon
ba
which probably never makes a lot of sense, except for tests. To stress the network even more, you can make the interval short and the message long, e.g.,
bd
sd 125 0 1 this_is_a_longish_beacon_message
sb d 1 10000
ba
If you let the beacon run for a while in this fashion and then deactivate it (bd), you will see that it takes some time for the output (the acknowledgements) at node 5 to die out. This lets you see the impact of buffering: the beacon has stopped at the source, but the network still has to deal with its legacy for a while.
Note that the numerical ID of a beacon message (call it the reference number) is increased by one each time the beacon message is sent by its source. This is handy for cross-referencing sends and receives for a large quantity of interleaving messages. Furthermore, if you use 0 for this ID, it will be replaced on each send with the time-stamp of the beacon's departure, for more elaborate measurements (see Imagination is the limit).
## The master node and its beacon
We have been using node 5 as the primary source (and sink) of all traffic in the network. If such a node naturally occurs in an application, we call it the master node. You can make node 5 the formal master by executing:
m 1
i.e., setting the master attribute of the node. You will see the node's colour in the ROAMER window change to blue. The node will be sending periodically and indefinitely, at 30-second intervals, a standard (broadcast) beacon telling all nodes its identity as the master. This way a node willing to send a report message to the sink will know which node to address. Additionally, the master beacons help TARP to organize forwarding in such a way that the paths leading to the master are (in some sense) preferred. Informally speaking, this is accomplished by making the distributed knowledge about those paths more difficult to forget.
The standard beacon messages are not reported by the nodes. In the model, you can see their traces in the ROAMER window, but they are completely hidden from your view in the real network.
You can revoke the master status of a node with:
m 0
Also, when another node becomes the master (and sends its master beacon), the previous master node abdicates politely (as soon as it receives the beacon).
## ODR messages
This message type is intended to send messages along specific, hard, point-to-point paths. Try this (assuming we still are at node 5):
so 99 1 4 3 2 1
The command defines an ODR message whose numerical ID is 99 and whose route goes through nodes 4, 3, 2, 1 and back (the first 1 requests the backward direction as well). The last node on the list can be viewed as the final destination. If you open UART windows at the nodes along the message's path and execute:
xo
at node 5 to actually dispatch the message, you will see a report of its delivery at every step. Again, don't be surprised if the message gets lost at some hop. The ODR mechanism offers no built-in reliability.
Once an ODR message reaches its final destination, it continues along the same path backward to the original sender, if the acknowledgement was requested. A full success of an ODR message with ack=1 is thus marked by its return to the sender.
Here is a sample forwarding report as seen at node 2:
4227: odr #99 [1.3.4]:
 0: (5 0 0)
 1: (4 105 0)
 2: (3 103 0)
 3: (2 105 105)<
 4: (1 105 0)
The time stamp and message ID are followed by three numbers separated by periods. They stand for (in this order):
- The direction indicator with 0 meaning forward and 1 meaning backward. In the present case, we are looking at a message travelling backward towards the sender.
- The number of hops counting from the source (of the original message).
- The hop range, i.e., the total number of hops.
The current node is marked with <. The numbers in parentheses stand for the node ID, the RSS (received signal strength) indication of the packet as received by the node on its way forward, and the backward RSS indication of the packet.
The distribution of nodes in our network model (as well as the channel parameters) have been chosen to represent an “optically” reasonable ad-hoc wireless setup with longish (but not prohibitively long) distances between neighbouring nodes. In this environment, there is a fair nonzero chance that a packet will fail to make a given hop. You can witness that by trying various multi-hop ODR messages: the more the hops, the smaller the chance that the packet will make it through the entire round trip.
You can turn an ODR message into a beacon, e.g.,
sb o 10 1000
will make a beacon of the current ODR message to be sent 1000 times at 10-second intervals. You still have to activate the beacon (ba) to actually send the messages out.
## Trace messages
The role of trace messages is to track TARP routes. They travel to specific destinations, possibly over multiple hops, being routed by TARP rules, and report information about the hops taken along the way. Here is a sample command to define a trace message:
st 77 10 0 0
It says that we want to send the message with ref# 77 to node 10, see a report of the backward route (taken by the destination's reply) at the source (this is the meaning of the third argument), and we impose no limit on the number of hops (the last zero). When you issue the above command at node 5 and follow it by:
xt
to actually send the message, you may see at node 5 something resembling this:
Trace #77 to 10 dir 0 hco 0
15988: tr(10) #77 10 4 4:
 10 104*
 1 104
 3 99
 4 104
 5 104
The first line shows up immediately after you issue the xt command; the subsequent lines only appear when (and if) a reply arrives from node 10. Following the time stamp, we see in the second line the number of the responding node, i.e., the recipient of the original message (in parentheses), reference# 77 followed by the (internal) message type (10 means a reply to a trace message requesting a backward route report), followed by the number of hops taken by the forward message, followed in turn by the number of hops taken by the reply (they need not be the same under TARP, even though they agree in the above case). The subsequent lines list the nodes visited by the reply including the RSS indications of the received packets. The value at node 10 (the sender of the reply message) marked by an asterisk shows the RSS of the packet carrying the forward message.
The second (direction) argument of st can take these values:
0	Back trace displayed at the sender only.
1	Forward trace displayed at the destination.
2	Forward trace displayed at the sender. The trace will be collected by the recipient and stored in the response message.
3	Bidirectional trace displayed at the sender. The trace shows the full circle made by the original message + the reply.

For example, a trace message defined like this:
st 88 10 3 0
and sent from node 5 may trigger the following output (at node 5):
Trace #88 to 10 dir 3 hco 0
22715: tr(10) #88 6 5 4:
 6 103
 7 104
 8 105
 9 104
 10 104
 9 105
 8 105
 6 98
 5 103
Note that in this case the backward path is shorter than the forward one.
When the trace is shown at the destination, as for a message defined this way:
st 99 10 1 0
the output only contains the forward path, e.g.,
22847: tr(5) #99 5 164 4:
 4 103
 3 104
 1 101
 10 102
Of the last three numbers in the first line, only the very last one is meaningful: it gives the total number of hops; the first number of the triplet is the trace message type (there is a few types involved), and the second one is the message's (internal) sequence number. Note that when a similar message appears at the source (when the direction argument of st is 2), we get two hop counts, e.g.,
22904: tr(10) #99 8 4 5:
 4 102
 3 104
 1 99
 10 105
*5 104
The first count (4) applies to the forward message: the path (from node 5) was 4, 3, 1, 10, while the second one (5) refers to the reply carrying the forward trace information. The last line shows the RSS of the reply packet received by node 5.
When you limit the hop count of a trace message, with a nonzero fourth argument of st, the message will be quietly dropped if its forwarding would exceed the limit. In such a case, you will see no trace of the message.
## Communication parameters
The global communication parameters of the node, known as the TARP parameters, can be changed with the sT (set TARP) command. You probably don't want to change them unless you understand what you are doing. Note that you can render the node inoperable with a broken setting.
The command accepts four parameters with the following meaning (in this order):
plev	The power level for transmission. The range is 0 (the minimum power) through 7 (full power). The default power level is 7.
rx	This is a binary flag telling whether the receiver should be on (1) or off (0). The default setting is 1 (on). Note that by switching the receiver off you basically incapacitate the node. While it can still be used to transmit (e.g., beacons), it won't be able to receive or forward anything.
fwd	This is a binary flag telling whether the node should act as a forwarder (1) or not (0). The default setting is 1. When you disable forwarding, the node will be able to transmit and receive packets, but it will not be retransmitting received packets destined to other nodes.
slack	This parameter determines the degree of fuzziness (or redundancy) of TARP's paths. The permissible values are 0 (no fuzziness), 1, and 2. The default setting is 1.
rte	This is a number between 0 and 3 telling how eagerly TARP should explore alternative routing opportunities. 1 means most eager, 3 means least eager, and 0 means “switched off”, i.e., no exploration at all. The default setting is 2.
tlev	This parameter can be 0, 1, or 2 and can be viewed as a TARP activation switch. The interpretation is: 0 – no TARP, pure flooding only restricted by the hop count limit of 10; 1 – flooding (as for 0) additionally restricted by elimination of duplicate packets, 2 – TARP. The default setting is 2.

One potentially useful parameter to experiment with is plev. For example, reducing the transmission power may have a similar effect to increasing distances between nodes. Beware that different power levels used by different nodes may create asymmetric links (one of the two directions between a pair of nodes being more opportune than the other direction), which may degrade TARP's performance.[5]
[5] Generally, when some communication parameters are changed, it makes sense to change them globally for all nodes in the network. Production networks have the capacity to carry out such global changes consistently upon an OSS request passed to the network through the master node.
If you ever decide to change some of the communication parameters, then you may want to make the change non-volatile across resets (power-down/power-up). This can be accomplished by writing the new set of parameters to the so-called FIM (Flash Information Memory) from where they will be reloaded on every reset. Consider this sequence of commands:
sT 0
Fw
The first one changes the first (i.e., plev) communication parameter to zero, i.e., selects the lowest transmission power. The second command makes the change non-volatile by writing the new set of values to FIM. Now, when the node reboots, it will see that FIM contains something that looks like a correct setting of the communication parameters and it will use that setting instead of the factory defaults.
You can see the current configuration of the communication parameters by issuing sT without arguments. Here are two more operations on FIM:
F
Lists the configuration of parameters stored in FIM, and:
Fe
Erases the configuration stored in FIM, thus forcing a fallback to factory defaults on the nearest reset. The factory defaults are:
FIM(128): plev 7 rx 1 fwd 1 slack 1 rte 2 tlev 2
This is the line produced by F on a virgin node.
Command q resets the node, t switches on / off (default) display of odr messages on transient nodes.

# Experimenting with real nodes
## Quick Start
Connect two nodes, say #4 and #5 to USB ports (the black wire should be on the antenna's side):

Note the power switch in “USB position” (toward the antenna). If the node is supplied from batteries, the switch should be in “battery position” away from the UART pins and the antenna. As soon as the node is powered up on default settings, the yellow LED goes ON. The other two LEDs, barely visible under the continuous yellow, signal the moments of RF transmission (green) and reception (red).
If a terminal emulator is connected to the corresponding COM port of the PC prior to connecting the node, the startup and welcome sequence should appear (also after every reset/re-power), similar to:
PicOS v3.6/PG121115A-WARSAW, (C) Olsonet Communications, 2002-2012
Leftover RAM: 9222 bytes
CC1100: 1, 842.3MHz, 0/200kHz=842.3MHz
Netting commands:

s (set / show) disp, odr, trace, beacon, TARP:
sd [ref# dst ack <string>]
so [ref# ack hop1 ... hop9]
st [ref# dst [ dir(3) [ hops(0) ]]]
sb [ (d,o,t) freq (<64) volume (>0) ]
sT *CAREFUL* [plev rx fwd slack rte tlev]
s (show node status)

Beacon operations:
ba (activate)
bd (deactivate)

Transmit:
x(d,o,t)

FIM operations:
Fw(rite)
Fe(rase)
F (read)

m(aster) [1/0]
t(ransient) [1/0]
h(elp)
q(uit)

Note that the RF module is configured for the European ISM band. With nodes #4 and #5 on, you may now explore Netting, e.g., starting with the simple scenarios described in “Display messages”.
Note that Windows 7 (and Vista) is likely to find the FTDI drivers on its own. Windows XP usually requires pointing it to a directory with the manually downloaded drivers. Here is the official web page of the manufacturer: http://www.ftdichip.com/Drivers/VCP.htm.
## Programming nodes
To reflash a node, you have to connect to it the FET programmer. The cable should be connected in such a way that its red stripe is on the east side (assuming the JTAG socket facing north). This means that the red stripe is pointing towards the down edge of the box in the figure below. Also, if you are using Windows, the Elprotonics utility must be installed.

## Imagination is the limit
As already mentioned, the message beacon allows unattended (logged) operations and diverse stress-tests. Everything will become clear with a bit of practice; here we'd like to illustrate the mechanism of morphing the (special) message reference number 0 to time stamps on the beacon. For example, consider this ODR beacon amounting to a 5-fold ping-pong exchange between nodes 1 and 10. The nodes were placed next to each other, which you can deduce from the very high RSS indications. The terminal emulator was connected to node 1. Underlined sequences correspond to user input, the remaining ones are the node's responses. The listed reports cover the history of the first beacon message (of the 12 messages to be sent altogether).

so 0 1 10 1 10 1 10 1 10 1 10
Odr(9) #0 ack 1 [10 1 10 1 10 1 10 1 10]
sb o 5 12
Beac o(2) freq 5 0 of 12
t1
ba
Beac o(2) freq 5 0 of 12
597: odr #596 [0.2.9]:	*A
 0: (1 0 0)
 1: (10 235 0)
 2: >(1 236 0)
 3: (10 0 0)
 4: (1 0 0)
 5: (10 0 0)
 6: (1 0 0)
 7: (10 0 0)
 8: (1 0 0)
 9: (10 0 0)
597: odr #596 [0.4.9]:
 0: (1 0 0)
 1: (10 235 0)
 2: (1 236 0)
 3: (10 235 0)
 4: >(1 236 0)
 5: (10 0 0)
 6: (1 0 0)
 7: (10 0 0)
 8: (1 0 0)
 9: (10 0 0)
597: odr #596 [0.6.9]:
 0: (1 0 0)
 1: (10 235 0)
 2: (1 236 0)
 3: (10 235 0)
 4: (1 236 0)
 5: (10 235 0)
 6: >(1 235 0)
 7: (10 0 0)
 8: (1 0 0)
 9: (10 0 0)
597: odr #596 [0.8.9]:
 0: (1 0 0)
 1: (10 235 0)
 2: (1 236 0)
 3: (10 235 0)
 4: (1 236 0)
 5: (10 235 0)
 6: (1 235 0)
 7: (10 235 0)
 8: >(1 236 0)
 9: (10 0 0)
598: odr #596 [1.8.9]:
 0: (1 0 0)
 1: (10 235 0)
 2: (1 236 0)
 3: (10 235 0)
 4: (1 236 0)
 5: (10 235 0)
 6: (1 235 0)
 7: (10 235 0)
 8: (1 236 235)<	*B
 9: (10 235 0)
598: odr #596 [1.6.9]:
 0: (1 0 0)
 1: (10 235 0)
 2: (1 236 0)
 3: (10 235 0)
 4: (1 236 0)
 5: (10 235 0)
 6: (1 235 236)<
 7: (10 235 235)
 8: (1 236 235)
 9: (10 235 0)
598: odr #596 [1.4.9]:
 0: (1 0 0)
 1: (10 235 0)
 2: (1 236 0)
 3: (10 235 0)
 4: (1 236 236)<
 5: (10 235 235)
 6: (1 235 236)
 7: (10 235 235)
 8: (1 236 235)
 9: (10 235 0)
598: odr #596 [1.2.9]:
 0: (1 0 0)
 1: (10 235 0)
 2: (1 236 236)<
 3: (10 235 235)
 4: (1 236 236)
 5: (10 235 235)
 6: (1 235 236)
 7: (10 235 235)
 8: (1 236 235)
 9: (10 235 0)
599: odr #596 [1.0.9]:	*C
 0: (1 0 235)<
 1: (10 235 235)
 2: (1 236 236)
 3: (10 235 235)
 4: (1 236 236)
 5: (10 235 235)
 6: (1 235 236)
 7: (10 235 235)
 8: (1 236 235)
 9: (10 235 0)

In the line marked *A (on the right), we see the first turn of the beacon, i.e., the first arrival of the message back at node 1. The first value in parentheses (the time stamp of the report) should be compared against the second value (representing the departure time of the beacon at the source). We see that the beacon's departure must have occurred close to the boundary of second 596, because the report's time stamp is 597 (the second count has advanced), while the entire round trip (all five turns) takes no more than 3 seconds (this is the difference between the last report time and the beacon's departure time at the source). Note that the report including the line marked with *B was made at time 598, which is the first advancement over the 597 noted at the first turn (line *A). This lets us claim that the 8 hops from *A to *B took very close to 1 second. Indeed, the next advance of the time stamp is noted at line *C, again 8 hops later, which adds credibility to our 8-hops-per-second estimate.

We see the full ODR path, and the sb request asks for 12 of them (so there are 11 similar sequences to follow). If you do long hop chains, especially with round trips, choose a beacon frequency as to leave up to 2-3s per hop, to allow per hop retries. The above ODR beacon made 18 hops in 3s but with weaker RF transmit power, interference, or longer distances between nodes it can take 10 times longer.

Feel free to explore various tasks with combinations of the above. Just to put things in some practical perspective:

Display: this kind of message for multi-hop delivery is typical in ad-hoc networking applications.

Beacon with requested ACK: well approximates the functionality of an audit process resending important messages for end-to-end reliability.

Trace: for setup verification, site surveys, and some sophisticated host-based location algorithms. Usually, the application cares about message delivery, not about the path it took.

ODR: a strange beast, doesn't exist in 'regular' applications. However, it can be used for:
- approximation of tube networking, although it is a bit misleading
- verification and visualization of distributed collaboration scenarios involving specific subsets of nodes
- troubleshooting, especially if the RF channel can be suspected of problems
- ODR with delays or per node triggered functionality may serve as a distributed operator-prescribed audit
Note that the feature is rather useless with mobile nodes.
## Terminal emulators
We recommend our piter (http://www.olsonet.com/REPO/piter.zip), which is a simple emulator intended for raw OSS access to our nodes. The program needs no installation. Just unpack it and execute. When the program starts, it presents a window to select the parameters of the COM port. If you know the identity of the COM port, you can select it from the menu. Otherwise, try pressing Scan, which should narrow down the menu to the list of COM ports that can be opened on your PC. Make sure the right COM port is selected in the top menu. For the remaining parameters, choose: Speed: 9600, Prot: Direct, Rlen: 82, Bin: unchecked, no Add-ons. Then press Proceed (or Save & Proceed).[6] If everything is OK, you should be able to talk to the node. Try h or q (followed by Enter) in the bottom (input) line. You should see in response the command menu. If that doesn't work, try powering the node down and up again.
[6] The program stores its settings in C:/Users/your_user_name/.piterrc.
A general purpose terminal emulator, which we also use sometimes, can be downloaded from http://www.olsonet.com/REPO/Terminal.zip. Feel free to give it a try, but remember that while piter is line-oriented (with the line format already tuned to the expectations of the node program), Terminal is character oriented and you have to make sure that all its parameters are properly configured: Baud rate: 9600, Data bits: 8, Parity: none, Stop bits: 1, Handshaking: none, Receive: select ASCII, Transmit: check CR=CR+LF. Then select your COM port and press Connect. One problem of Terminal (surfacing in the context of our LittleLab) is its the character-orientedness. With piter, if you make a mistake in an input line, you can correct it before sending the line to the node (which only happens when you hit the Enter key). With Terminal, as soon as you have typed a character, it goes to the other side, so you cannot revoke it and correct the line. Even though the Backspace key seems to work at first sight, the strokes are in fact sent to the node as characters of their own. The node's program is not prepared to deal with them, so the best it can do is to signal a command error.