# Ariadne

Technical Note

Version 0.1
January 2012

© Copyright 2012, Olsonet Communications Corporation.
All Rights Reserved.

TOC

# Introduction
Ariadne descends from Survey, with its functionality focused on all aspects of RTLS. We intend to have it as a set of tools integrated for experiments with our location engine (See the LOCATION documents) but also as a general surveying and RTLS testing tool.
We drop the notion of pegs and tags - all the nodes run the same software; however, the functional equivalent of a tag or peg can be achieved simply by switching some (software) modules on or off.
Any node can become a master (coordinator, sink, sniffer) and this role is not restricted just to a single node in the setup.
For operational simplicity, we don't restrict power budget and communicating readiness, so battery life would not exceed 2-3 days of continuous operations. If Ariadne's functional blocks prove to be generally useful, they will morph into libraries. Then, the power-budget- eeprom- and other-functionality- related blocks will be built.
By default, we assume 1-hop range, as anything larger would be impractical for envisioned setups. As any other parameter, this can be set to an arbitrary radius, with all the networking consequences. In sequel, we use the word 'setup' instead of 'network' to describe a cooperating set of nodes, mainly for this reason.
# Functional Blocks: Outline

All the functionality consists of independent blocks that can be switched on / off. The operations are driven by sets of parameters, some of them common for several blocks. All the commands can arrive via the serial or RF interface; I don't know if commands via RF will be functional in the 1st version.

Sniffer

It listens to RF and considers outputting through (serial) OSSI whatever it hears. The actual output is filtered and formatted by several options.

Commander

It sends to other nodes commands entered via (serial) OSSI, retries, listens to the acks,, etc. In other words, this node is used to configure and operate a setup.

Commander and Sniffer together form a traditional Master functionality, although this Master is nonexclusive within a setup.

Pinger

Driven by several parameters, it originates periodic pings, gathers their echoes and sends out ping reports. Within a complete Ariadne system, it either listens to its centrally calculated position or cooperates with an associated device (over Bluetooth SPP) for local calculations.

Echoer

Responds to pings.

All these blocks can be switched on /off to form the desired functionality. A couple of storyboards show the most natural setups:

# Storyboards
## Survey
We describe an experiment easy to setup anywhere: in- or out-door, office, conference floor, picnic area, etc. Here, we use nine nodes in a rectangular room. We set four peg-like nodes in the corners. They are immobile, with preset coordinates. The other four nodes will be tag-like, moved around, to record an 'rssi map' for the grid of known points within the rectangle form by pegs. A dedicated node plays the role of a Master (Commander and Sniffer) connected to OSS (piter on PC).
Typical setup: The nodes are flashed with appropriate hardware identifiers, placed in the area to be surveyed, and switched on. We call the node attached to a serial terminal the Master. Although it can be any node, in this document the Master’s hardware id is 0xBACABACA. For (wasteful) simplcity and experiments with the appropriate functional divisions, this node doesn't take part in gathering location data, i.e. it is not a Pinger nor Echoer.
Hardware id is a unique 32-bit number. Local_ host or logical id is a settable unique identifier of a communicating node. However, for simplicity we overload the local_host with intended Cartesian coordinates. The ids are settable and may be interpreted off-line, so this is not a constraint. Local_host is initialized to lower two bytes of the hardware id. As an example, if we flash 4 nodes with hardware ids 0xBACA0101, 0xBACA0106, 0xBACA0606, 0xBACA0601 and interpret the coordinates in meters, we have the setup provisioned as a 5x5 meter square with the nodes as its vertexes. VUEE/Survey/sim.xml configures this setup it in VUEE, and in this document we paste all output from VUEE running it. The application should run on any node type (was roughly tested on WARSAW nodes). Genihex utility is handy for creation of images with good hardware id, e.g. 'genihex Image_peg.a43 BACADEAD BACA0101 1'.
Note a diversion from the model described in the LOCATION documents: we don’t deal with tags within a grid of pegs, and we measure vectors as opposed to distances. However, this approach can be trivially folded into the data sets expected in the current and evolving versions of the algorithm.
The version 0.4 introduces the 'all out' flag to help distinguish between two main applications: 'site survey' and 'tag among pegs'. The former gathers data about all 2* (n -1)! unidirectional links between n immobile nodes (within the network and UART limits, of course). The latter is aimed at measuring unidirectional links between selected (possibly mobile) nodes (tags) and the grid of other nodes (pegs). It significantly reduces the number of reported links to 2*n per selected node. The node is chosen in this mode if its logical id is in [1, 0xFF] range which in our notation is equivalent to x = 0 in the Cartesian pair (x, y). The master's 'all out' flag is propagated in msg_master messages that coordinate the sessions, so the whole setup may be very dynamic and is open to interesting experiments by mere id manipulations. See the 'sa' command.
## States
Under the Master’s control, the nodes automatically cycle through prescribed experiments, changing pertinent parameters in unison. The Master outputs all data through UART. (Local data storage was ruled out as more restrictive. However, in certain scenarios (e.g. a jungle setup) it may be revisited as a more suitable approach.)
Init (ST_INIT: Red LED ON)
In this state, the nodes await msg_master messages to set the parameters and transition to the Warm-up state. The Master awaits user commands. After the boot, Master automatically starts the experiment on stored or default data, if there is no user input for 10 seconds.
Warm-up (ST_WARM: Green LED blinking)
The nodes, set with the intended parameters, await the first msg_ping to move to the Cycle state and start a new barrage of messages. The Master repeats msg_master for a specified period of time, and then seeds the chaotic exchange of the msg_ping messages.
Cycle (ST_CYC: Green LED ON)
All nodes monitor their resources under a heavy traffic of broadcast messages. The forwarding is switched off, but each node responds with msg_ping to every msg_ping it receives, creating avalanche of packets and heavy congestions. As a side effect, we get an excellent opportunity to study behavior of relevant PicOS modules, especially VNETI and memory and process management. The Master outputs all it can through UART in a non-blocking way that again let us observe the system coping with a cancerously growing resource demand. After a specified period of time, the Master moves to the Warm-up state, updates its parameters and starts issuing msg_master messages to update and move all the other nodes to the Warp-up state as well.
Cooling (ST_COOL: Blue (yellow) LED ON)
At any time on the user command, the Master may move to the Cooling state and start issuing msg_silence messages that make other nodes to follow to Cooling as well, with switched off transmitters. This state is intended for manual intervention and is not part of the regular cycle (init -> warm-up -> cycle -> warm-up -> cycle … -> cycle -> init).
RF silence triggers the Master’s transition from Cycle to Warm-up with new parameters, shorting the regular cycle. It is intended for studying nodes at verge of the RF range, extreme RF conditions, etc.
If nodes discover that they are engaged in an unobserved (no UART out) traffic or there is an extended period of silence, they reset.
Msg_master messages are transmitted also on default channels and rates, to allow nodes to be added to ongoing experiments.
Nodes that don't receive any messages or don't receive a message from the master for the whole cycle duration auto-reset to become receptive again, on default settings.

# OSSI: Commands and output to OSS

In this document, the OSS is a terminal attached to the Master via RS232. However, in the next versions we’ll follow with the description of processing of the gathered data as input into the LOCATION algorithms. We hope the praxis and the algorithms will inspire each other in their evolutions.
The data is output in a flexible and on the fly changeable format. Creating new formats is trivial, so catering to any OSS demand is reduced to the collection of required data items.
## Cycle (ping) reports
All msg_ping messages the Master receives within allowed limitations are output via UART. This is the HI (human interface) output:
Ping 211
[6 1 0] 144 (173) (6, 6)->(6, 1)
[6 1 0] 144 (189) (6, 1)->(1, 1)

The ping came at 211 Master’s time. It reports RSSI (144) for the messages sent from the node (6, 6) to (6, 1) and from (6, 1) to (1, 1). Note that the last node is always the node with the attached terminal. At that time, the node (6, 6) already sent 173 and node (6, 1) 189 pings within this session. The session is set for RF power level 6, rate 1 (10kbps), and channel 0.
Raw format contains the same data, but in one line, separated by blanks.
If SEQ_NO_BUNDLES is nonzero, the output is reformatted for further processing and includes sequence numbers. For example:
-- 7 3 0	10 15 60	0 12 148	38 41
-- 7 3 0	0 12 19	1 1 123	43 41
As before, each ping reaching the master, generates two lines, as the 2nd comes free to describe how the master node sees the 'intermittent' node.
First two (arbitrary) characters mark ping's output, say for:
 egrep “^--” log | sort > log_to_analyze.
The “7 3 0” marks the “session”, here power level 7, rate 3 (200kbps), channel 0. If multiple sessions are run, it is important to distinguish them for separate analysis.
Next triples, e.g. 10 15 60 0 12 148 shows that the packet #60 from node (10,15) was received by node (0,12) with RSSI 148. As before, we decode coordinates from node ids. Nodes with X=0 are meant to be 'mobile' and subject to off-line mapping, e.g. the node C (0,12) in a given experiment should be mapped to position (8,12) in the experiment shown in the nov21.xml model.
The last two entries, e.g. 38, 41mostly are superfluous: first is the packet 'bounce counter', sort of age marker, the second is the master time the packet was output. It may be useful to spot sequence number looping, which shouldn't occur in regular experiments, but can happen in long or somewhat abnormal sessions... Note that we are still just describing ideas of experiments; likely, some things will change with the feedback from the results interpretation.
Each session (cycle) is summarized with the statistics output:
Stats for local hid - lh BACA0101 - 257 (1, 1):
 Attr pl 7-0 (6), rate 0-3 (1), ch 0-10 (0)
 Counts m(197) r(0) t(284) u(427), touts: sil 3, warm 5, cyc 15
 Time 212 (sstart 196), Flags 000C, Mem: free 3276, min 3132
 State 2 RF 6

The first line shows the local (as opposed to remote) hardware id and local host with the node coordinates derived from it. (The data is available from any node in the experiment, after switching the UART ON; see the su command below.)
The attribute line shows ranges and the session values for power level, rate, and channel number.
The 3rd line shows the counters:
- m - # of ping messages sent out
- r - # of messages dropped because of the RX buffer congestion
- t - # of messages dropped because of the TX buffer congestion
- u - # of messages dropped because of the UART congestion
In the present version, congestions are defined by constants at compilation time, but this may be changed easily. In fact, any constant within the praxis can be trivially turned into a settable parameter.
The 4th line shows when the session started and ended, the flags, free memory, and the minimum memory available since the boot. Memory is shows in 2-byte words. The flags are:
- flags & 1 – autoack on (not used)
- flags & 2 – an internal flag between TARP and the praxis (master change)
- flags &4 – UART output is ON
- flags & 8 – HI (human interface) format
- flags & 16 – praxis internal (no response to seeding messages)
- flags & 32 – all out: site survey as opposed to specific location assessments

The last line shows the current state and RF status.
States:
- 0 – Init
- 1 – Warm-up
- 2 – Cycle
- 3 – Cooling
- 4 – Off (at boot)

RF status:
- status & 1 – Rx ON
- status & 2 – Tx ON
- status & 4 – nonempty Tx queue
## Commands
Welcome screen:
***Site Survey 0.2***
Set / show attribs:
      from:	sf [pl [ra [ch]]]
      to:  	st [pl [ra [ch]]]
      id:  	si x y <new x> <new y>
      uart:	su [0 | 1]
      fmt: 	sy [0 | 1]
all out:	sa [0 | 1]
      stats:	s [x y]

Timeouts / intervals:
      t [<silence> [<warmup> [<cycle>]]]

Execute Operation:
      silence:    os
      go:         og
      master:     om
      auto:       oa
      erase:      oe

Help: h
Optional trailing parameters can be omitted. Parameters that should be ignored (but are followed by significant ones) should be entered as '-1'.
### Commands set / show:
All set / show commands end with the statistics data displayed.
Set / show from: sf [pl [ra [ch]]]
Parameters:
pl           RF output power level. The mapping is CC1100-specific defined in PATABLE[]. The dBm values are unclear at the moment, 0 is likely –20, 2 is 0, and 7 is 10 dBm. Range [0, 7], defaults to 7.
ra           Encoded transmission rates: 0: 5kbps, 1: 10kbps, 2: 38.4kbps, 3: 200kbps. Defaults to 0.
ch           One of the 256 channels available. Range [0, 255], defaults to 0.

Set / show to: st [pl [ra[ch]]]
As in sf, with defaults 0, 3, 255, respectively. Note that iterating over the parameters is allowed in any order.
Set / show id: si x y x’ y’
Addresses the node (x, y) and changes its coordinates to (x’, y’). The node responds with the statistics data. This may be useful if the node is moved during an experiment.

Set / show uart: su [0 | 1]
UART output OFF | ON. At the initialization and a command attempt, if the node has its UART OFF, “I’m mute!” warning appears.
Set / show format: sf [0 | 1]
Changes the ping output format. 0: raw, 1: HI. Defaults to 1.
Set / show all out: sa [0 | 1]
If set, the 'all out' options is propagated to all nodes, and all 2* (n – 1)! unidirectional links are being reported. Defaults to 0.
Statistics: s
Displays statistics data formatted as described in the ‘Cycle (ping) reports’ section above.

### Timeouts / intervals:

      t [<silence> [<warmup> [<cycle>]]]
Sets and shows the cycle’s intervals, in seconds:
- silence: If no message is received for that many seconds, the Master moves to the next cycle Range [1, 15], defaults to 3.
- warmup: Number of seconds the msg_master messages set the next cycle. They’re sent every second. Range [1, 15], defaults to 5.
- cycle: Time the pings are being sent and reported for. Range [1, 255], defaults to 15.

### Execute Operation:

      silence:    os
      go:         og
      master:     om
      auto:       oa
      erase:      oe

- os: forces the nodes into the Cooling state
- og: go; usually after all the data is set
- om: this node will be the Master
- oa: save current settings into the EEPROM (for future runs)
- oe: erase EEPROM

We trust the praxis is simple enough to make examples and more details unnecessary, at least in the present version.

# Known Bugs & Pitfalls

There still are surprises on the RF interface. Since the praxis may be quite useful for gathering data, it is released as is, while the works continue.

Some of the info e.g. 'I'm mute!' is hastily output via diag() and is misplaced if there is pending regular output.