# The Reflow Praxis
(second [still tentative] version)

November 14, 2012

© Copyright 2011, 2012, Olsonet Communications Corporation.
All Rights Reserved.

This note is a crude description of an even more crude, tentative version of the Reflow praxis. If we decide that the effort is worthwhile, the praxis will be equipped with a GUI. The present UART interface will probably suffice for that purpose, i.e., I think that, in addition to providing a rough command-line user interface, it can also comfortably act as a programmatic interface between the GUI and a node running the praxis.

When connecting to the praxis from piter (or another terminal emulator), set the UART rate to 115200. We need a high UART communication rate to reduce the processing overhead, which may affect the accuracy of PWM timing.

External devices

The praxis assumes that its node has been interfaced to two devices:

- a MAX6675 thermocouple temperature sensor (PicOS driver: max6675.c)
- a PWM relay (e.g., a thyristor) driving the oven

The board configuration for the praxis is in BOARDS/WARSAW_REFLOW. See there for the relevant hardware options.

I have created a simple generic driver (pwm_driver.c) for the kind of PWM (pulse width modulation) control appropriate for a reflow oven. The idea is that the (default) total width of a control cycle is 1 second subdivided into 1024 slots corresponding to PicOS milliseconds. The control parameter is a non-negative integer number from 0 to 1024 with 0 meaning “off” and 1024 meaning “fully on”. Anything in between represents the respective fraction of full power. At the beginning of each second, the driver switches on the device (by pulling a pin) for the number of ticks equal to the current setting of the control parameter. Then, following that many ticks, the device goes off for the remaining number of ticks in the second. With the extreme settings (0 or 1024), the device never goes on or off (respectively).

The PWM “device” is visible to the praxis as an actuator (see board_pins.h in BOARDS/WARSAW_REFLOW). In the previous version of the board, you could switch the oven on and off manually (the control was binary). Now you can set the oven to any number between 0 and 1024. The previous (TESTS/REFLOW) praxis has been modified, such that its 'on' command accepts an optional argument defaulting to 1024 (so the new setup is compatible with the old praxis).

The thermocouple sensor requires calibration. The calibration data appears in options.sys in the praxis directory (the symbol THERMOCOUPLE_CALIBRATION) and consists of a sequence of pairs: <temperature, sensor reading> where the sensor readings must be strictly increasing and temperature must be non-decreasing. Feel free to modify the values if you know better. You can also add values in between to improve the accuracy (which is probably pointless). Note that temperature is expressed in degrees Celsius times 10, which formally gives us the precision of 1/10 of a degree. This is also how temperature is represented internally in the praxis and used in all calculations.

Command list

When started, the praxis shows this list of commands:

Commands:
 g s i d -> set parameters
 i b -> set integrator bound
 e -> erase profile
 p d t ... -> add profile entry
 s -> show parameters
 r -> run
 a -> abort
 o n -> set oven
 t -> read temp
Ready:

The same list will be shown in response to any invalid command, e.g., h[elp].

With the last two commands you control the oven manually and directly read the temperature. The argument of o is a number from 0 (oven off) to 1024 (full on). In response to t the praxis displays the current temperature readout in degrees (with one digit after the decimal point) as well as the raw value extracted from the sensor.

With the g command you can redefine the three parameters of the controller which are:

- the temperature span of the controller, s (which can be viewed as the equivalent of the proportional factor used in the previous version)
- the integral factor (i)
- the differential factor (d)
- the integral bound (b)

With e and p you can create profile data. The first command erases all the present profile data, while the second one adds one or more segments to the data set. A single segment is a pair of values <duration, temperature>, where duration is the segment's target duration in seconds and temperature is the target temperature at the segment's end.

The idea is that the duration of a segment is the desired amount of time until the target temperature is reached, i.e., it determined the intended slope of the segment's curve. However, the segment will only complete if the target temperature is in fact reached. For illustration, consider the sequence of segments of the default profile. You will see it, together with the default configuration of control parameters, when you issue the s command, which will produce this output:

S/I/D: 200 0 0, NPE: 6
 P0: 0 150.0
 P1: 101 183.0
 P2: 88 220.0
 P3: 37 183.0
 P4: 19 150.0
 P5: 0 80.0
Ready:

The profile consists of 6 segments. Note that the duration of segment 0 is zero seconds. This means that the purpose of the segment is to reach the target temperature (150 degrees in this case) as fast as possible (the temperature is the only criterion of the segment's completion). The duration of segment 1 is 101 seconds and the target temperature at its end is 183 degrees. The program will do its best to reach the target temperature in 101 seconds from the segment's commencement (the end of the previous segment). However, if the temperature cannot be reached that fast, the segment will extend, as required, until the target temperature is actually reached. If (by some accident, e.g., overshooting) the temperature is reached sooner, the segment will still take 101 seconds, so the specified duration should be viewed as a minimum.

Note that in this version of the praxis we specify segment durations rather than absolute time points in the entire run. We don't know how much time a run will take. Instead of trying to maintain a precise timing of the run, we focus on reaching the target temperatures within no less than the specified segment durations.

Note that the duration of the last segment is zero (similar to the first segment). It is a cooling segment meaning that we want to go down to 80 degrees as soon as possible (oven off). When that happen, the run will be considered done.

When you add a new segment to an existing profile, it is always appended at the end of the already existing list of segments. Also note that when inputting temperature values of profile points you specify degrees (with optional fractions) rather than tens of degrees.

A p command may specify an arbitrary number of points up to the limit of 24 (which is the maximum length of a profile). If you want to build a new profile, execute e first (which completely erases the previous profile). For example,

e
p 40 120 70 180.5 120 200 180 70

will yield this:

S/I/D: 200 0 0, NPE: 4
 P0: 40 120.0
 P1: 70 180.5
 P2: 120 200.0
 P3: 180 70.0
Ready:

With the argument-less command r you start the reflow cycle for the currently defined profile (and the current configuration of control parameters). While a cycle is being executed, the praxis displays a line every second providing some feedback about the process. Here is a sample sequence of such lines:

...
!T 8 [P=0,U=0,T=1500] 1341->1500, 814
!T 9 [P=0,U=0,T=1500] 1456->1500, 225
!T 10 [P=0,U=0,T=1500] 1456->1500, 225
!T 11 [P=1,U=112,T=1830] 1585->1500, 0
...

The number following !T is the current time (current second) of the cycle. This is followed by three numbers: P = the current segment number, U = the target time (second) at the end of the segment, T = the target temperature at the end of the segment. Then we have the current temperature (before the arrow) and the target temperature (after the arrow), both in degrees x 10. Finally, we see the setting of the oven's throttle, which is always between 0 and 1024 (1024 means full throttle).

The parameters

The three parameters of the control algorithm are:

S

The temperature span of the controller expressed in degrees x 10. If the target temperature at the time (according to the current segment's slope) exceeds the measured temperature by more than S, then the oven is set at full throttle. Otherwise, i.e., the difference is less than S, the controller tries to be more subtle setting the throttle proportionally to the difference, with the maximum falling on S. The minimum setting of S is 10 (corresponding to 1 degree). The default setting is 200 (corresponding to 20 degrees). Reducing S makes the controller more aggressive. The maximum value (probably way too large to be useful) is 1024.

I

The integral factor. The default value is zero, the range is 0 – 1024. Probably, it should be set to something nonzero, but not too large, say 10 – 200, to prevent undershooting.

D

The differential factor. The default value is zero, the range is 0 – 1024. Keep it zero until you see overshooting; then try something between 10 and 500.