# The Reflow Praxis
(a tentative version)

October 27, 2012

© Copyright 2011, 2012, Olsonet Communications Corporation.
All Rights Reserved.

This note is a crude first description of an even more crude, tentative version of the Reflow praxis. If we decide that the effort is worthwhile, the praxis will be equipped with a GUI. The present UART interface will probably suffice for that purpose, i.e., I think that, in addition to providing a rough command-line user interface, it can also comfortably act as a programmatic interface between the GUI and a node running the praxis.

When connecting to the praxis from piter (or another terminal emulator), set the UART rate to 115200. We need a high UART communication rate to reduce the processing overhead, which may affect the accuracy of PWM timing.

External devices

The praxis assumes that its node has been interfaced to two devices:

- a MAX6675 thermocouple temperature sensor (PicOS driver: max6675.c)
- a PWM relay (e.g., a thyristor) driving the oven

The board configuration for the praxis is in BOARDS/WARSAW_REFLOW. See there for the relevant hardware options.

I have created a simple generic driver (pwm_driver.c) for the kind of PWM (pulse width modulation) control appropriate for a reflow oven. The idea is that the (default) total width of a control cycle is 1 second subdivided into 1024 slots corresponding to PicOS milliseconds. The control parameter is a non-negative integer number from 0 to 1024 with 0 meaning “off” and 1024 meaning “fully on”. Anything in between represents the respective fraction of full power. At the beginning of each second, the driver switches on the device (by pulling a pin) for the number of ticks equal to the current setting of the control parameter. Then, following that many ticks, the device goes off for the remaining number of ticks in the second. With the extreme settings (0 or 1024), the device never goes on or off (respectively).

The PWM “device” is visible to the praxis as an actuator (see board_pins.h in BOARDS/WARSAW_REFLOW). In the previous version of the board, you could switch the oven on and off manually (the control was binary). Now you can set the oven to any number between 0 and 1024. The previous (TESTS/REFLOW) praxis has been modified, such that its 'on' command accepts an optional argument defaulting to 1024 (so the new setup is compatible with the old praxis).

The thermocouple sensor requires calibration. The calibration data appears in options.sys in the praxis directory (the symbol THERMOCOUPLE_CALIBRATION) and consists of a sequence of pairs: <temperature, sensor reading> where the sensor readings must be strictly increasing and temperature must be non-decreasing. Feel free to modify the values if you know better. You can also add values in between to improve the accuracy (which is probably pointless). Note that temperature is expressed in degrees Celsius times 10, which formally gives us the precision of 1/10 of a degree. This is also how temperature is represented internally in the praxis and used in all calculations.

Command list

When started, the praxis shows this list of commands:

Commands:
 g p i d -> set gain
 i b -> set integrator bound
 e -> erase profile
 p s t ... -> add profile entry
 s -> show parameters
 r -> run
 a -> abort
 o n -> set oven
 t -> read temp
Ready:

The same list will be shown in response to any invalid command, e.g., h[elp].

With the last two commands you control the oven manually and directly read the temperature. The argument of o is a number from 0 (oven off) to 1024 (full on). In response to t the praxis displays the current temperature readout in degrees (with one digit after the decimal point) as well as the raw value extracted from the sensor.

With commands g and i, you can redefine the four parameters of the controller which are:

- the proportional factor (p)
- the integral factor (i)
- the differential factor (d)
- the integral bound (b)

With e and p you can create profile data. The first command erases all the present profile data, while the second one adds one or more points to the data set. A single point is a pair of values <time, temperature>, where time is in seconds (from the beginning of a reflow cycle) and temperature is the target temperature at that time.

A default profile configured into the praxis is described in options.sys. You will see it, together with the default configuration of control parameters, when you issue the s command, which will produce this output:

G: 5 0 0, I: 2, P: 8
 P0: 60 100.0
 P1: 85 150.0
 P2: 180 150.0
 P3: 210 200.0
 P4: 240 246.0
 P5: 270 246.0
 P6: 300 150.0
 P7: 360 25.0
Ready:

The three values following G: are the three factors of the control algorithm (p, i, d, in this order), I: is the integrator limit, and P: tells the number of points in the profile data. If that number is nonzero, the points are subsequently listed as <time, temperature> pairs. Note that temperature values are shown in degrees with one digit after the decimal point.

When you enter profile data (with p), you augment the already existing configuration. For example, if you now say:

p 230 220.1
s

you will see:

G: 5 0 0, I: 2, P: 9
 P0: 60 100.0
 P1: 85 150.0
 P2: 180 150.0
 P3: 210 200.0
 P4: 230 220.1
 P5: 240 246.0
 P6: 270 246.0
 P7: 300 150.0
 P8: 360 25.0
Ready:

Note that the new point has been inserted into its proper place based on the time value (the set now consists of 9 points). If the specified time value coincides with one already present in the set, that point is overwritten (replaced) with the new one (so the total number of points remains unchanged).

Also note that when inputting temperature values of profile points you specify degrees (with optional fractions) rather than tens of degrees.

A p command may specify an arbitrary number of points up to the limit of 24 (which is the maximum length of a profile). If you want to build a new profile, execute e first (which completely erases the previous profile). For example,

e
p 40 120 70 180.5 120 200 180 10

will yield this:

G: 5 0 0, I: 2, P: 4
 P0: 40 120.0
 P1: 70 180.5
 P2: 120 200.0
 P3: 180 10.0
Ready:

With the argument-less command r you start the reflow cycle for the currently defined profile (and the current configuration of control parameters). While a cycle is being executed, the praxis displays a line every second providing some feedback about the process. Here is a sample sequence of such lines:

...
!11 124->224 50 (50, 50, 0, 0)
!12 124->240 58 (58, 58, 0, 0)
!13 124->255 65 (65, 65, 0, 0)
!14 124->271 73 (73, 73, 0, 0)
!15 202->287 42 (42, 42, 0, 0)
!16 202->303 50 (50, 50, 0, 0)
!17 202->319 58 (58, 58, 0, 0)
...

The number immediately following ! is the current second of the cycle. This is followed by the current and target temperature of the oven in degrees x 10 (current->target). The next value is the computed setting of the oven's PWM (between 0 and 1024). The values in parentheses indicate (respectively):

- the unbound control value, i.e., the oven setting derived from the algorithm, which need not be bounded to 1024; it gives an indication how desperate the controller is to bring the current temperature to the target
- the contributions of the three parts of the controller (P, I, D) to the computed oven setting; note that by default only the proportional (p) factor is nonzero, so the contributions of the I and D components are zero

We can see that the default p factor (5) is probably way to small (the PWM values appear too small compared to the temperature difference.

You can abort a cycle in progress by entering any command (which will subsequently execute). The abort (a) command does nothing (except for aborting a cycle, if one is in progress). When a cycle is aborted the oven is set to zero (off).

The parameters

I don't have the oven, so I can't experiment with the parameters to tune them for sensible operation. It is not clear whether that can be done at all with the present praxis. If not, we will have to modify the algorithm.

Basically, you can try some values for p, i, d, b and see what happens. Once you decide that they are close to what you want, you can put them as defaults in options.sys (the symbols starting with DEFAULT_). Here are my simplistic suggestions.

I would recommend to start by finding the best value of p with the remaining two factors set to zero. This will give you a ballpark of the sensible ranges for all the factors. Note that for as long as i is zero, b doesn't matter. Once you get something half-way decent with p alone, you will probably be seeing these problems:

1. undershooting: the algorithm behaves reasonably well when the temperature difference is high, but it slows down too rapidly when the target is close
2. overshooting: when you use a larger p, to be able to reach the target faster (e.g., while trying to improve 1), the algorithm tends to overshoot

To remedy 1, use a nonzero i. It is difficult for me to recommend anything specific, but the values shouldn't be too large. While technically the range of the factors is 0-1024, reasonable values for all of them should (probably) be below 100. For the integrator (while correcting for undershooting), there is a tradeoff between the values of i and b. A larger b may have the same effect as a larger i, but in a different sort of way. Note that the maximum for b is 10.

To correct for overshooting, try a nonzero d. It will have the effect of slowing down the controller when the observed reaction of the oven is high. The integrator, on the other hand, tends to speed up the controller when the difference between the current and target temperatures tends to persist. So the two are opposite in a sense: the integrator brings about speed (to quickly get close to the target), while the differentiator brings about caution (when the progress appears too rapid).